## Slide 1: XMPP as SBI implementation Tomek Osiński: Orange Labs, Warsaw, Poland Abdulhalim Dandoush: ESME Sudria engineering school, France
Project wiki: https://wiki.onosproject.org/display/ONOS/XMPP+as+SBI

## Slide 2: Agenda
Introduction
  BGP VPN architecture
  XMPP protocol
Design & implementation
Demo
Evaluation
Conclusions

## Slide 3: XMPP protocol
Features:
  XML-based
  Highly extensible
Core XMPP (RFC 6120):
  XMPP Stream
  XMPP Stanzas (IQ, Message, Presence)
  TLS/SASL
XMPP Extension Protocols (XEPs)
  https://xmpp.org/extensions/
XMPP Publish/Subscribe extension:
  Publish/Subscribe paradigm
  payload-agnostic
XMPP in the SDN area:
  OpenContrail

## Slide 4: Overview of MPLS/L3VPN-XMPP solution
https://tools.ietf.org/html/draft-ietf-l3vpn-end-system-06
VM
Hypervisor with vRouter
Server or Compute Node
Tenant VRF, Policies, etc
Encapsulation Tunnel
(MPLSoGRE, or VXLAN)
XMPP (BGP)
Datacenter
Route Reflector
BGP
Provider Network
L3 VPNs for Inter-Site Connectivity Traffic segmentation in the WAN MPLS over MPLS label encapsulation tunnels BGP route signaling
Contrail Virtual Networks in Datacenters Traffic segmentation in the LAN MPLS over GRE or VXLAN label encapsulation tunnels XMPP (with BGP payload) route signaling
Protocols, Architecture
Customer Site
CE Router
PE Router
Customer VRF
Encapsulation Tunnel
OpenStack Cloud Manager
Contrail Controller
SOURCE OPNFV/OpenContrail

## Slide 5: Proposed solution for ONOS
Physical Network (no changes)
ONOS
XMPP SBI
Physical Host
with Hypervisor
vRouter
VM
VM
VM
VM
WAN, Internet
Gateway
Interacts with network elements for VM network provisioning and ensures uptime
Juniper vRouter: Virtualized routing element handles localized control plane and forwarding plane work on the compute node
Gateway: MX Series (or other router) or EX9200 serve as gateway eliminating need for SW gateway & improving scale & performance
Emulated vRouter for testing objective
Nova Agent
BGP

## Slide 6: The concept of XMPP as SBI
We use XMPP Publish/Subscribe extension
XMPP PubSub introduces new communication model between devices and SDN controller
SDN controller as a communication bus
XMPP is a „container protocol”
How it differs from OpenFlow?

## Slide 7: Design & Implementation
XMPP as SBI for ONOS

## Slide 8: Solution design
ONOS with XMPP SBI and Route Server
Virtual routers in the data plane
BGP over XMPP
vRouters subscribes to ONOS for a VPN topic (SUBSCRIBE)
vRouter publishes BGP NLRI associated with VPN (PUBLISH)
Peer vRouters are notified about new virtual interface (UPDATE)

## Slide 9: XMPP as SBI implementation
XMPP as SBI implementation is main contribution of the project
Main functionalities of XMPP SBI:
  Asynchronous, non-blocking XML parsing
  Decoding/encoding XMPP messages
  Abstracting underlaying devices
  Maintaining the state of connected devices
  XMPP events distribution to Providers
  Device Provider
  Extensible implementation to add new XMPP extensions (e.g. Publish/Subscribe)

## Slide 10: Implementation architecture
Principles:
  extensibility
  re-use of ONOS abstractions and subsystems
Protocols layer
  decomposed into core XMPP and XEP implementation
Providers layer
  Route provider (RouteService subsystem)
  Flow provider (FlowRuleService subsystem)
Route Server application
  make use of RouteService, FlowRuleService
  VpnInstanceService

## Slide 11: Tests of XMPP SBI
Unit tests coverage
  Merged with master branch
Functional tests using Python sleekxmpp library:
  Establishing XMPP stream
  Closing XMPP stream
  XMPP SUBSCRIBE / UNSUBSCRIBE test cases
  XMPP PUBLISH / RETRACT test cases
Validation based on:
  RFC 6120 - XMPP Core specification
  XEP-0060 - XMPP Publish/Subscribe extension
  IETF draft - BGP-signaled IP/VPNs system

## Slide 12: Evaluation
XMPP as SBI for ONOS

## Slide 13: SBI’s functionality
XMPP is a general-purpose protocol!
  BGPoXMPP is Virtual interface-oriented (VRF tables)
  “container protocol”, it’s all about data model design
OpenFlow is flow-oriented (multiple-flow-tables)
PCEP is used to compute the paths and requires IGP and TE protocols
Our BGP over XMPP is positioned between OpenFlow and PCE …
NETCONF, SNMP | OpenFlow | BGP over XMPP | LISP | PCEP | BGP, OSPF, IS-IS
Device management | Flow-oriented traffic engineering | Routing (L3VPN), Bridging (EVPN) | Tunneling | Traffic engineering mainly with legacy devices | East-west communication with legacy systems

## Slide 14: Performance of OpenFlow vs XMPP
Experiment setup:
  Single ONOS instance - control plane performance
  up to 5 vRouters (compute nodes)
  Scenario 1:
    1 VM per compute node
    Increasing number of compute nodes (1..5)
    ICMP ping between each unique pair of VMs
  Scenario 2:
    2 compute nodes
    Increasing number of VMs (1..5)
    ICMP ping between each unique pair of VMs

## Slide 15: Performance of OpenFlow vs XMPP
Experiments:
  Single instance - control plane performance (done)
  ONOS cluster - control plane performance (to be done)
  Data plane performance (to be done)
  Control plane delay (to be done)

## Slide 16: Use case
We propose BGP over XMPP, but XMPP is agnostic to use case!
 | Main use case | Area of usage | Approach | Scalability
BGP over XMPP | L3VPN, EVPN | Intra-DC, Inter-DC (with BGP) | Evolutionary | Good
OpenFlow | Traffic engineering, NAT, ACL, etc., multi | Intra-DC, Inter-DC | Revolutionary | Limited
PCEP | TE, path compute and tunnels | Inter-DC (with IS-IS or OSPF) | Evolutionary | very Good

## Slide 17: Conclusions
XMPP as SBI for ONOS

## Slide 18: Summary
XMPP SBI for ONOS is ready!
  BGP over XMPP as a new control plane solution
  extensible architecture
  XMPP as “container protocol”
Evaluation:
  BGP over XMPP positioned between OpenFlow and PCEP
  In case of intra-DC connectivity BGP over XMPP performs much better than OpenFlow!
Further work:
  Complete performance analysis
  Research paper publication
  Integration with OpenContrail vRouter
  Integration with OpenStack

## Slide 19: Demo
XMPP as SBI for ONOS

## Slide 20: Demo scenario
Instantiate ONOS controller and 3 vRouters
Run Mininet hosts and attach them to vRouter (with overlapping IP addresses)
Test connectivity between “red” hosts
Test connectivity between “blue” hosts

## Slide 21: Demo recording

## Slide 22: Q&A
Thank you!

## Slide 23: Functionality (2/2)
BGP over XMPP vs. OpenFlow
  Both are used to exchange routing information inside DC
  OpenFlow is flow-oriented (multiple-flow-tables), while BGPoXMPP is Virtual interface-oriented (VRF tables)
BGP over XMPP vs. PCEP
  Both are used at the edge of network
  PCEP cannot be applied inside DC, but few devices need to communicate with the controllers
  BGP over XMPP allows to span VPN across multiple DC