## Slide 1: SPRING-OPEN & ONOS
Saurav, Srikanth, Sangho
1 /12 /15

## Slide 2: Issues
Group handling
Pipeline handling
Use of intent framework
Configuration management
Treatment and Selector extensions
Stats/CLI/Karaf-CLI/GUI/multi-part-msg/SLAVE

## Slide 3: 1. Group handling
Group table is a major feature of OF 1.3
Today’s hardware has support for groups
SR uses two kinds of groups – SELECT & INDIRECT
SR uses an optional feature of OF 1.3 called group-chaining
SR may use FRR group in the future
ONOS needs to prepare for groups, but also meters and queues (and pipelines)
  OF1.3 based SDN is intrinsically low-level
  Use of these features are app controlled

## Slide 4: How SR uses Groups?
Hardware Switch
Driver
Core
App
Config
Default groups
(auto-created during handshake)
avoids races
improves performance
Special groups
(policy-driven)
Device subsystem
Ports
Groups
Add/delete/modify groups
Flow-rule subsystem

## Slide 5: Groups Proposal
Need a new Group Subsystem
  that allows app to treat groups just like flows
  Add/delete/modify groups on demand according to app needs
  Allows any ONOS instance to create group in any switch
Need Device Subsystem (service) to expose groups
  like it exposes ports today as an intrinsic property that is fundamental to the topology map broadcast to everyone
  Allows any app (on any ONOS instance) to query Device manager about the groups on the device
  Receive device-events on the addition/deletion/mod of groups on the device

## Slide 6: Issues
Group handling
Pipeline handling
Use of intent framework
Configuration management
Treatment and Selector extensions
Stats/CLI/Karaf-CLI/GUI/multi-part-msg/SLAVE

## Slide 7: 2. Pipeline Handling
Can’t avoid it if working on ASIC based hardware
Can’t (totally) abstract it away to the app
Going to become more and more important

## Slide 8: Sample Pipelines (TTPs) – 1/3
SPRING-OPEN TTP
Ingress
Port
Incoming
Packet
VLAN
Flow
Table
Termination
MAC Flow
Table
Unicast
IPv4 Routing
Flow Table
z
MPLS
Forwarding
Flow Table
ACL
Policy
Flow
Table
Apply
Actions
-push/pop
-TTL mpls
-Set
-Output
-Group
Outgoing
Packet
z
Group Table Entries:
L3 Unicast
MPLS Unicast
ECMP
Pkt. +
Meta-
Data +
Action
Set {}
Egress
Port
or
Group

## Slide 9: Sample Pipelines (TTPs) – 2/3
Broadcom OF-DPA 1.0

## Slide 10: Sample Pipelines (TTPs) – 3/3
Broadcom OF-DPA 2.0

## Slide 11: How SR uses pipelines?
Driver
Core
App
Partially aware of pipeline (IP/MPLS/ACL tables & some groups)
Completely aware of pipeline (OF messages, Goto/Clear/ Write or Apply Actions)
Pre-populates statically populated tables
IOFSwitch
IOF13Switch
ext
OFSwitchImplBase
impl
OFSwitchImplSpringOpenTTP
ext
ext
ext
OFSwitchImplCpqd
OFSwitchImplDell
impl

## Slide 12: Pipelines proposal
Most of ONOS pipeline unaware – can stay that way
  Driver for TTP & pipeline awareness
  App should be configured for specific pipeline to use as part of solution/service deployment
FlowRuleProvider
  exposes table-awareness
  writes directly to switch using sw.write() methods for simple 1.0 switches
  uses driver-methods to write to 1.3 switches that support a specific TTP
  allows option to make flow-rules stateless (i.e. does not copy flowrules to other instances)

## Slide 13: Issues
Group handling
Pipeline handling
Use of intent framework
Configuration management
Treatment and Selector extensions
Stats/CLI/Karaf-CLI/GUI/multi-part-msg/SLAVE

## Slide 14: 3. Use of the Intent Fw
Technically feasible to implement Compiler and Installer for SR
Framework currently does not provide option to be stateless
App does not need to worry about replication or install/recovery state-machine
Heavyweight state-machine, hard to debug, parts of SM not implemented
If purpose is reuse, SR compiler and installer would likely only be used for SR
If purpose is ‘the chance to resolve between flow-rules’  very hard, impossible given OF 1.3 and pipelines
✔
✗
✔
✗
✗
✗

## Slide 15
How SR does routing?
Default Routing
  done by app using dst-rooted, per-router, in-trees calculation and stage-by-stage installation to guarantee loop-free updates
  completely stateless – upon failure new next hops are determined and installed overwriting old rules – does not require knowledge of old rules
  Flow-space separated per controller instance using subnets  allowing parallel operation
Policy Routing
  done by app in single controller instance
  statefull

## Slide 16: Issues
Group handling
Pipeline handling
Use of intent framework
Configuration management
Treatment and Selector extensions
Stats/CLI/Karaf-CLI/GUI/multi-part-msg/SLAVE

## Slide 17: 4. NetworkConfigManager
Channel
Config Service
Network
Config
Mgr.
Config file
Startup
Config
CLI/ REST
Running
Config
Topology Manager
hosts
switches
links
Store
ONOS Instance
ONOS Instance
ONOS Instance
Startup
Config
Startup
Config
Startup
Config
Running
Config

## Slide 18: Filtering Logic
Restrict switches?
Yes
Default Deny
No
Default Allow
Has Config?
Has Config?
No
No
DENY
ACCEPT
Allowed?
Yes
Allowed?
Yes
No
DENY
DENY
No
Yes
Yes
ACCEPT & ADD
ACCEPT & ADD
Allow list
Deny list

## Slide 19: Issues
Group handling
Pipeline handling
Use of intent framework
Configuration management
Treatment and Selector extensions
Stats/CLI/Karaf-CLI/GUI/multi-part-msg/SLAVE